## Slide 1
VLSI / FPGA PROJECT · FIRST REVIEW
FPGA-Based Real-Time
Audio Classification
Edge sound detection system — no cloud, no latency
Platform: Cyclone IV E · DE2-115 Tool: Quartus Prime
Sample Rate: 48 kHz FFT Size: 512-point Mode: Single Floating Point
FFT
512pt
Float

## Slide 2
PROBLEM STATEMENT
430M+
Hearing impaired
globally
WHO estimate
100%
Emergency sounds
missed daily
without assistive tech
>500ms
Cloud latency
risk for alerts
unacceptable for safety
The Challenge
1
Deaf and hard-of-hearing users cannot perceive critical environmental sounds — doorbell, fire alarm, attention signals.
2
Existing solutions depend on smartphones and cloud APIs, introducing unacceptable latency and failure points.
3
A dedicated edge device running entirely on FPGA hardware solves both problems: sub-10ms response, zero cloud dependency.

## Slide 3
SYSTEM ARCHITECTURE
sample_gen
512-sample
frames
▶
fft_block
Time →
Frequency
▶
magnitude
block
Complex →
Amplitude
▶
detection
block
Band energy
classifier
▶
output
block
LED + 7-seg
display
AXI-Stream handshake (valid · ready · sop · eop) across all stages
Frequency Band Mapping · Δf = 48000 ÷ 512 = 93.75 Hz/bin
Sound
Frequency
Bins
Detection Logic
Alarm
~800 Hz
6 – 8
energy_alarm > THRESHOLD
Doorbell
~1 kHz
9 – 13
energy_doorbell > energy_alarm
Attention
~3 kHz
29 – 35
energy_attention is max of all three

## Slide 4
KEY VERILOG MODULES
Classifier
detection_block.v
– Accumulates FFT magnitude into 3 frequency bands per frame
– Compares band energies at EOP with adjustable threshold
– Outputs 2-bit sound code: 00=silence, 01=alarm, 10=doorbell, 11=attention
– Non-overlapping bands: Alarm 6–8, Doorbell 9–13, Attention 29–35
Math
magnitude_block.v
– Extracts amplitude from IEEE-754 complex FFT output
– Approximation: max(|real|, |imag|) — avoids FP multipliers on FPGA
– Strips sign bit and compares 31-bit unsigned values
– Preserves magnitude ordering — valid for relative comparison
IP Wrapper
fft_block.v
– Wraps Vivado-extracted xfft_0 with Altera sink/source naming
– Translates AXI-Stream ↔ Altera streaming port conventions
– Generates source_sop from output frame counter
– Forward FFT, 512-point, single floating-point, natural order

## Slide 5
PERFORMANCE METRICS · SIMULATION RESULTS
10.67 ms
End-to-end latency
512 samples @ 48 kHz
21.33 ms
Throughput latency
1024 cycles @ 48 kHz
93.75 Hz
Frequency resolution
Δf = 48000 ÷ 512
< 100 ms
Target met
Real-time threshold
Output Encoding — DE2-115 Board
Code
Sound
LED
7-Seg
Frequency
2'b00
Silence
All off
n
—
2'b01
Alarm
LED0
A
~800 Hz (bins 6–8)
2'b10
Doorbell
LED1
d
~1 kHz (bins 9–13)
2'b11
Attention
LED2
t
~3 kHz (bins 29–35)

## Slide 6
UPGRADE ROADMAP · HACKATHON READINESS
Layer 1
Bug fixes
▸ Separate band ranges — no overlap between Alarm & Doorbell
▸ Add mag_valid delay — align timing of valid/sop/eop with magnitude
Layer 2
Reliability
▸ 5-frame majority voting — reject transient noise
▸ Confidence score on HEX display (e.g. 85% doorbell)
Layer 3
Demo impact
▸ INMP441 I2S MEMS mic — replace ramp with real audio
▸ UART live dashboard — stream results to PC in real time
Layer 4
Narrative
▸ Use case: assistive tech for hearing impaired (430M globally)
▸ Pitch: edge safety device, wearable-ready, zero cloud

## Slide 7
CONCLUSION · NEXT STEPS
What is built
✓
Complete 5-stage FPGA streaming pipeline
✓
512-point FFT with floating-point support
✓
Band-energy based sound classifier
✓
Full testbench with watchdog & monitor
✓
Vivado-to-Quartus FFT migration wrapper
Next steps
1
Hardware test on DE2-115 board
2
Connect INMP441 I2S microphone
3
Tune THRESHOLD for real audio
4
Add multi-frame majority voting
5
Prepare IEEE paper / demo video
"Real-time FPGA edge audio classifier — assistive tech for the hearing impaired. No cloud. No latency. Just hardware."